## Slide 1: CFS ECI Technical Overview
Steve Lentine

## Slide 2: Overview
Framework which makes integrating externally-generated code into CFS environment easier
  Targets:
    Autogenerated code
    Legacy code
    Hand-written algorithms
CFS ECI
Core Flight System External Code Interface
Notes: ECI is a tool which is part of the CFS ecosystem. Not an app in-and-of-itself… framework which creates CFS apps from externally-produced code.

## Slide 3: ECI History
Originally developed as part of the Simulink Interface Layer (SIL)
  SIL had 2 parts:
    Extension to code generation pipeline
    Generic wrapper code to integrate generated code into CFS
  ECI is the generic wrapper code from the SIL
Split into separate project from SIL in 2018
  Better communicates its non-Simulink uses
  Formalizes specification of interface

## Slide 4: ECI Architecture
External Code
Interface Definition
External
Code
Messages Out
Event Flags
Messages In
cFE Software Bus
Event Processing
Other Apps / Mission Ops
cFE Event Services
Mission Ops
- Queue Cmd Message
- Provide Seq#
- Error Check Message
SCH
Execute
Housekeeping
Table Management
cFE Table Services
Mission Ops
cFE Time Services
cFS Time
Fetch Time
Status Flags
CFS
ECI
External Code
Input memory
Parameter memory
Output memory
Init/Step/Term functions

## Slide 5: Compiling ECI App
Interface definition (eci_interface.h) is compiled with external code and ECI wrapper code to produce a cFS application
ECI Wrapper Code
eci_app.c
eci_app.h
<app_name>.o
App Compilation
cFS Application
Interface Definition
eci_interface.h
External Code

## Slide 6: System Architecture
Event
Services
Stored
Command
CFDP File
Transfer
Scheduler
Packet
Manager
Executive
Services
Time
Services
File
Manager
Commands
cFS Applications
Real-time Telemetry
Communication
Interfaces
Mission Applications
1553 Bus
Support
File downlink
Software
Bus)
Instrument
Manager
Command
Ingest
Telemetry
Output
1553
Hardware
Memory
Manager
Data
Storage
Mass
Storage
File System
Table
Services
Limit
Checker
Space
Wire
Instruments
Core Services/Applications
Inter-task Message Router (Software Bus)
External Code
ECI
Interface
Header
Notes: Typical system architecture… CFS bubble chart
ECI integrates code as a CFS app via wrapper

## Slide 7: ECI Services for external code
Initialization, execution, and termination of application
Input/Output message management with cFE Software Bus
Table management with cFE Table Services
Housekeeping counter management
Event services registration and event triggering
Critical Data Store (CDS) nonvolatile storage of data
Feature set grew from requirements of Ames and GSFC missions: LADEE, NICER, GEDI, PACE
Notes: ECI has extensive heritage in GNC applications for a number of Goddard and Ames missions.
Note: ECI was known as SIL for those projects, but it’s the same code.

## Slide 8: ECI Interface Overview
ECI uses a memory-only interface to the external code
  Passive interface for external code
    No callbacks/API/etc which would require modifying external code
ECI defines an interface standard which external code must provide (via separate header file)
ECI’s wrapper code utilizes this interface definition to automatically initialize and manage the proper cFS interfaces
Notes: Core principle: Avoid modifications to original code (which breaks heritage, requires effort in implementing/re-testing/re-qualifiying)
Memory-only interface: integrator at memory/variables in external code and maps them to CFS interfaces

## Slide 9: External Code Interface Definition
External code interface implemented via header file
  Contains:
    Pointers to input/output messages
    Pointers to parameter data structures
    Pointers to flags for status flags and events
  Macros/data structures in this header file are used during ECI compilation

## Slide 10: CFS Interfaces – Input Messages
ECI uses interface specification to:
  Subscribe to message IDs on the software bus
  Each cycle, check for new messages
  Fill sequence counter field
  Validate length, ApID, CmdCode
  Copy messages to external code for processing
  Maintain message received counters
  Responds to boilerplate commands (NoOp, ResetCtrs, etc)
  For commands: maintain command queue
  TODO: Config setting to strip header

## Slide 11: CFS Interfaces – Output Messages
ECI uses interface specification to:
  Register message ID’s with software bus
  Check sendMessage flag to determine whether to send message
    Supports Asynchronous/Periodic messaging
  Copy packet payload from external code
  Fill header of outgoing packet (Apid, Length, Sequence Counter, Timestamp)
  Send on software bus
  Increment packet sent counter

## Slide 12: CFS Interfaces – Parameter Tables
ECI uses interface specification to:
  Register parameter tables with CFS table services
  Upon receipt of management request from table services:
    Loads new table
    Executes table validation function (if specified)
    If passed, activates table
  Dump table to telemetry packet

## Slide 13: CFS Interfaces – Events
ECI uses interface specification to:
  Register events with CFE Event Services
  Issue event when flag is set

## Slide 14: CFS Interfaces – Status Flags
ECI uses interface specification to:
  Maintain latch flags indicating if flags have been set
  Concatenate flags into bitfields and telemeter in ECI housekeeping packet

## Slide 15: Compatible External Code Architectures
Calling:
  External code must provide a single “Step” function to be called each execution
  External code may also provide an initialization function and a termination function to implement setup/teardown
  Step/Init/Term functions must not take any arguments (void/void interface)
I/O:
  Each message (input or output) must be a contiguous region of memory
  Must have global scope in external code
Parameters:
  Each parameter table must be a contiguous region of memory
  Must have global scope in external code
All interfaces must be declared at compilation (can’t register new messages/events/etc at runtime)
Notes: Flexibility with respect to system setup can mitigate the effects of these limitations (ie, if several pieces of data needs to be output which are not in contiguous memory, output as multiple packets and have downstream apps subscribe to each packet or use HK app to combine them)

## Slide 16: External Code Sources
SIL (Simulink Interface Layer):
  Extends Simulink code generation pipeline to automatically generate interface definition header file
  Fully automates code integration with ECI
42:
  Examining feasibility of integrating 42 models into CFS
Handwritten Code:
  No known examples yet
Legacy Code:
  No known examples yet

## Slide 17: ECI Interface Standard

## Slide 18: Interface Standard
Interface is specified via a header file (eci_interface.h)
  Agnostic to source (hand-written or autogenerated) as long as it follows standard
Interface header is compiled with external code and ECI framework to produce a CFS application

## Slide 19: Interface Standard: Code Calling Interface
3 macros define functions to call during lifecycle of application:
  MODEL_FCN_INIT: Called once at startup to initialize code
  MODEL_FCN_STEP: Called every app execution
  MODEL_FCN_TERM: Called once at termination to cleanup
Functions must not take any parameters
Interface header example:
#define MODEL_FCN_INIT MY_APP_initialize();
#define MODEL_FCN_STEP MY_APP_step();
#define MODEL_FCN_TERM MY_APP_terminate();

## Slide 20: Interface Standard: Input Messages
Table ‘ECI_MsgRcv’ defines external code input messages
1 entry per message
For each message:
  Message ID
    Specified by FSW developer/integrator
  Pointer to message in external code’s memory
  Size of message
  Command Buffer
    Only used for command messages, otherwise Null
  Null
    Only used for output messages
Terminated with NULL entry

## Slide 21: ECI_MsgRcv Example:
Entry Contents: {appID, pointer, size, cmdBuffer, NULL}
Interface header example:
static my_cmd_t my_cmd_queue[CMD_MSG_QUEUE_SIZE];
static ECI_Msg_t ECI_MsgRcv[] = {
{ MY_APP_MY_CMD_MID, &my_cmd_pointer, sizeof(my_cmd_t), &my_cmd_queue[0], NULL },
{ MY_APP_MY_TLM_MSG, &my_tlm_pointer, sizeof(my_tlm_t), NULL, NULL },
{ 0, NULL, 0, NULL, NULL }
};

## Slide 22: Interface Standard: Output Messages
Table ‘ECI_MsgSnd’ defines external code output messages
1 entry per message
For each message:
  Message ID
    Specified by FSW developer/integrator
  Pointer to message in external code’s memory
  Size of message
  Null
    Field not used for output messages
  Message send flag
    True: Send message this cycle
    False: Don’t send message this cycle
    Null: Send every cycle
Terminated with NULL entry

## Slide 23: SIL_MsgSnd Example:
Contents: {appID, pointer, size, NULL, sendflag}
static ECI_Msg_t ECI_MsgSnd[] = {
{ MY_APP_MY_MESSAGE_MID, &my_message, sizeof(my_message_t), NULL, NULL },
{ MY_APP_MY_MESSAGE2_MID, &my_message2, sizeof(my_message2_t), NULL, sendMyMessage2 },
{ 0, NULL, 0, NULL, NULL }
};

## Slide 24: Interface Standard: Parameter Tables
Table ‘ECI_ParamTable’ defines external code parameter tables
1 entry per table
For each table:
  Pointer to table in external code’s memory
  String containing name of table
  String containing description of table
  String containing table filename
  Size of table
  Pointer to table validation function
Terminated with NULL entry

## Slide 25: ECI_ParamTable Example:
Contents: {pointer, name, description, fileName, size, validationFcn}
#define DO_PARAM_TBL 1
param_tbl1_t * param_tbl1;
param_tbl2_t * param_tbl2;
static ECI_Tbl_t ECI_ParamTable[] = {
{ &(param_tbl1), “MY_APP_PARAM_TBL1", “My app’s param table 1", “MY_APP_PARAM_TBL1.tbl", sizeof(param_tbl1_t),
&param_tbl1_validate},
{ &(param_tbl2), “MY_APP_PARAM_TBL2", " My app’s param table 2", "MY_APP_PARAM_TBL1.tbl", sizeof(param_tbl2_t),
NULL},
{ 0, 0, 0, 0, 0, 0 }
};

## Slide 26: Interface Standard: Event Messages
Table ‘ECI_Events’ defines external code event messages
1 entry per event
For each event:
  Number of data points
  Event ID (unique to app)
  Event type (debug, info, error, critical)
  Event mask (output filter)
  Event Flag (Boolean indicating to send event)
  Event Message (fprintf-style string to send)
  Location string (identifying where in code message originated)
  Up to 5 data values to include in message
    Unused data values ignored
Terminated with NULL entry

## Slide 27: ECI_Events Example:
Contents: {numData, EventID, eventType, eventFlag, eventMessage, eventLocation, dataValue1, dataValue2, dataValue3, dataValue4, dataValue5}
#define ECI_EVENT_TABLE_DEFINED 1
static const ECI_Evs_t ECI_Events[] = {
{ EVENT_message1_ID, my_event1_id, eventType, CFE_EVS_NO_MASK, sendEvent1Flag,
“Event1 message! Data value is: %f”, “myfcn()", &myDataVal, 0, 0, 0, 0
},
{ 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0 }
};

## Slide 28: Interface Standard: Status Flags
Table ‘ECI_FDC’ defines external code critical data
1 entry per event
For each event:
  Flag ID
    Unique to app
  Boolean Flag
Terminated with NULL entry

## Slide 29: ECI_FDC Example:

## Slide 30: Interface Standard: CDS Telemetry
Table ‘ECI_CDS’ defines external code critical data
1 entry per event
For each event:
  String containing name of CDS block
  Size of CDS block
  Pointer to CDS block
Terminated with NULL entry

## Slide 31: ECI_CDS Example:
Interface in progress

## Slide 32: Interface Standard: Macro Definitions
Must define following macros:
  App Information:
    ECI_MAIN
    ECI_NAME_UPPER
    ECI_NAME_LOWER
    REVISION_NUMBER
    ECI_CMD_PIPE_NAME
    ECI_DATA_PIPE_NAME
  Message IDs:
    ECI_FDC_MID
    ECI_CMD_MID
    ECI_PERF_ID
    ECI_TICK_MID
    ECI_TICK_HZ
    ECI_HK_MID

## Slide 33: ECI Operation

## Slide 34: ECI Command Interface
Range of FcnCode designated as ECI commands
  Any command in that range is processed/executed by the ECI framework (not passed to external code)
  Any command outside that range is passed to external code for execution

## Slide 35: ECI Execution Cycle
Receive Tick
Check for new input messages and process
  Execute ECI commands if received
Call external code step function
Send output messages
  Send HK if HK request received

## Slide 36: ECI Performance ID’s
At start of external code step function
ToDo: Find out if any others

## Slide 37: Execution Management
Each application subscribes to a TICK message that, when received, triggers execution of the external code’s step function.
Scheduler puts out tick messages that represent different frequencies of execution.
To control execution order, tick messages may be the output messages of other cFS applications. This allows for application execution to be chained among applications executed at the same frequency.

## Slide 38: Interfacing Autogenerated Code
SIL (Simulink Interface Layer) extends Simulink code generation pipeline to generate eci_interface.h for a model
  Fully automates generation of interface definition
  Used on GSFC missions: NICER, GEDI, PACE
May be possible to autogenerate interfaces for other types of code generation pipelines, but need defined use cases
  Rational Rhapsody?

## Slide 39: ToDo
Finish writing this document
  Example CDS, Status flags
  Describe execution cycle
  Describe ECI command handling
Implement configuration to add header (for use cases where external code doesn’t allocate space for header, which is probably common)
Implement configuration to strip header (for use cases where external code doesn’t allocate space for header, which is probably common)
Write actual interface spec
Retool unit tests to start from non-SIL interface definition?
Example eci_interface.h for trivial piece of hand code
Find widely-available implementation of some useful algorithm and work up example